## Slide 1: COMPUTER ARCHITECTURE
Harvard and von neumann

## Slide 2: Abstraction of computing

## Slide 3: Overview
  Architecture (Machine organization) overview
CPU
Harvard
von Neumann
CISC vs. RISC

## Slide 4: Computer COMPONENTS
Major components of a computer
  Central Processing Unit (CPU)
  memory
  Bus
    to move information from one component to another
    divided into three sub-buses, one each for data, addresses and control signals
  Peripheral devices

## Slide 5: CPU
The Central Processing Unit ( CPU)
  Often referred to as the “brain” of the computer.
  Responsible for controlling all activities of the computer system.
  CPU are mounted is mounted on a Motherboard along with most of other electronics
Features
  performs arithmetic and logical operations
  synchronous operation

## Slide 6: CPU
The three major components of the CPU are:
    1. Arithmetic Unit (Computations performed)
    Accumulator (Results of computations kept here)
    2. Control Unit (Has two locations where numbers are kept)
    Instruction Register (Instruction placed here for analysis)
    Program Counter (Which instruction will be performed next?)
    General-purpose registers, etc.
    3. Instruction Decoding Unit (Decodes the instruction)

## Slide 7: memory
Memory
  stores programs and data
  organized as
    bit
    byte = 8 bits (smallest addressable location)
    word = 4 bytes (typically; machine dependent)
  instructions consist of operation codes and addresses
oprn
oprn
oprn
addr 1
addr 2
addr 3
addr 2
addr 1
addr 1

## Slide 8: Computer COMPONENTS
Major components of a computer
  Central Processing Unit (CPU)
  memory
  Bus or I/O System
    to move information from one component to another
    divided into three sub-buses, one each for data, addresses and control signals
  *Peripheral devices e.g. secondary storage
v

## Slide 9: BUSES
Function
  to move information from one component to another
  divided into three sub-buses, one each for data, addresses and control signals
Types
  Address bus
  Data bus
  Control Bus
v

## Slide 10: Computer Architecture
Architecture is concerned with
  internal structures of each
  Interconnections - speed and width
  relative speeds of components
Balance is often critical execution speed and connections

## Slide 11: Von Neumann
Institute for Advanced Studies machine (1947)“von Neumann machine”
This model of the typical digital computer is often called the von Neumann computer.
  Programs and data are stored in the same memory: primary memory.
  The computer can only perform one instruction at a time.
  Separate CPU and memory distinguishes programmable computer.
Memory holds data, instructions.
Central processing unit (CPU) fetches instructions from memory.
  ALU performs transfers between memory and I/O devices
  note two instructions per memory word
Notes: Named after John von Neumann,
Princeton, he designed a
computer architecture whereby
data and instructions would be
retrieved from memory,
operated on by an ALU, and
moved back to memory (or I/O)
This architecture is the basis for
most modern computers (only
parallel processors and a few
other unique architectures use
a different model)
Hardware consists of 3 units
  CPU (control unit, ALU, registers)
  Memory (stores programs and data)
  I/O System (including secondary storage)
Instructions in memory are executed sequentially unless
a program instruction explicitly changes the order

## Slide 12: Von Neumann
Named after John von Neumann, Princeton, he designed computer architecture whereby data and instructions would be retrieved from memory, operated on by an ALU, and moved back to memory (or I/O)
This architecture is the basis for most modern computers (only parallel processors and a few other unique architectures use a different model)
Hardware consists of 3 units: CPU (control unit, ALU, registers) , Memory (stores programs and data) and I/O System (including secondary storage)
Instructions in memory are executed sequentially unless a program instruction explicitly changes the order
Notes: Named after John von Neumann,
Princeton, he designed a
computer architecture whereby
data and instructions would be
retrieved from memory,
operated on by an ALU, and
moved back to memory (or I/O)
This architecture is the basis for
most modern computers (only
parallel processors and a few
other unique architectures use
a different model)
Hardware consists of 3 units
  CPU (control unit, ALU, registers)
  Memory (stores programs and data)
  I/O System (including secondary storage)
Instructions in memory are executed sequentially unless
a program instruction explicitly changes the order

## Slide 13: VNA
main memory
Input- Output Equipment
Arithmetic - Logic Unit
Program Control Unit
op code
address
CPU
(Central Processing Unit)
Input
Units
Output
Units
Primary Memory

## Slide 16: VARIATIONS
single pathway used to move both data and instructions between memory, I/O and CPU
  the pathway is implemented as a bus
  the single pathway creates a bottleneck
    known as the von Neumann bottleneck
  A variation of this architecture is the Harvard architecture which separates data and instructions into two pathways
  Another variation, used in most computers, is the system bus version in which there are different buses between CPU and memory and memory and I/O

## Slide 17: OPS
The von Neumann architecture operates on the fetch-execute cycle
  Fetch an instruction from memory as indicated by the Program Counter register
  Decode the instruction in the control unit
  Data operands needed for the instruction are fetched from memory
  Execute the instruction in the ALU storing the result in a register
  Move the result back to memory if needed

## Slide 18: Harvard architecture
Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data.
Originated from Harvard Mark I relay-based computer,
  stored instructions on punched tape (24 bits wide) and data in electro-mechanical counters (23 digits wide).
  had limited data storage, entirely contained within the data processing unit,
  provided no access to the instruction storage as data,
  made loading and modifying programs an entirely offline process.

## Slide 19: The Harvard Architecture (2)
In a computer with a von Neumann architecture (and no cache), the CPU can be either reading an instruction or reading/writing data from/to the memory.
  Both cannot occur at the same time since the instructions and data use the same bus system.
In a computer using the Harvard architecture, the CPU can read both an instruction and perform a data memory access at the same time, even without a cache.
A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway.

## Slide 20: The Harvard Architecture (3)
In a Harvard architecture, there is no need to make the two memories share characteristics. In particular, the word width, timing, implementation technology, and memory address structure can differ.
In some systems, instructions can be stored in read-only memory while data memory generally requires read-write memory.
Instruction memory is often wider than data memory.

## Slide 21: Harvard architecture
CPU
PC
data memory
program memory
address
data
address
data

## Slide 22: Harvard Architecture Example
Block Diagram of the PIC16C8X
Notes: http://www.seattlerobotics.org/encoder/may97/picchip.html

## Slide 23: Modified Harvard Architecture
The Modified Harvard architecture is very like the Harvard architecture but provides a pathway between the instruction memory and the CPU that allows words from the instruction memory to be treated as read-only data.
  This allows constant data, particularly text strings, to be accessed without first having to be copied into data memory, thus preserving more data memory for read/write variables.
Special machine language instructions are provided to read data from the instruction memory.
Standards-based high-level languages, such as the C language, do not support the Modified Harvard Architecture, so that in-line assembly or non-standard extensions are needed to take advantage of it.
Most modern computers that are documented as Harvard Architecture are, in fact, Modified Harvard Architecture.

## Slide 24: von Neumann vs. Harvard
Harvard can’t use self-modifying code.
Harvard allows two simultaneous memory fetches.
Most DSPs use Harvard architecture for streaming data:
  greater memory bandwidth;
  more predictable bandwidth.

## Slide 25: CISC v RISC
CISC = Complex Instruction Set Computer
RISC = Reduced Instruction Set Computer

## Slide 26: RISC vs. CISC
Complex instruction set computer (CISC):
  many addressing modes;
  many operations.
Reduced instruction set computer (RISC):
  load/store;
  pipelinable instructions.

## Slide 27: CISC vs. RISC (continued)
Historically, machines tend to add features over time
  instruction opcodes
    IBM 70X went from 24 opcodes to 185 in 10 years
    same time performance increased 30 times
  addressing modes
  special purpose registers
Motivations are to
  improve efficiency, since complex instructions can be implemented in hardware and execute faster
  make life easier for compiler writers
  support more complex higher-level languages

## Slide 28: CISC vs. RISC
Examination of actual code indicated many of these features were not used
RISC advocates proposed
  simple, limited instruction set
  large number of general purpose registers
    and mostly register operations
  optimized instruction pipeline
Benefits should include
  faster execution of instructions commonly used
  faster design and implementation