## Slide 1: CMP1101: DIODE LOGIC

## Slide 2: Logic Gates
A logic gate is an elementary building block of a digital circuit.
  Most logic gates have 2 inputs and 1 output.
    The inputs or output (terminals) of a logic gate can take on one of 2 states:
      Low (0 or False), approximately 0V
      High (1 or True), approximately +5V
    The results of the input and corresponding output of a logic gate are tabulated in a Truth Table.
  The logic state of a terminal can change often as the circuit processes data.
  There are 7 basic logic gates
    NOT, OR, AND, NOR, NAND, XOR and XNOR

## Slide 3: NOT Gate
Popularly referred to as the logical inverter.
It serves the purpose of reversing the logic state.
Symbol:
Truth Table:
Input | Output
0 | 1
1 | 0

## Slide 4: OR Gate
Derives its name from the fact that it behaves like the logical inclusive “or”.
  The output is true if either or both of the inputs are true.
  If both inputs are false, then the output is false.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 5: AND Gate
The AND gate acts in the same manner as the logical “and” operator.
  The output is true when both inputs are true, otherwise the output is false.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: NOR Gate
Is a combination of the OR gate followed by an inverter.
  Its output is true if both inputs are false.
  Otherwise, the output is false.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 7: NAND Gate
Operates as an AND gate followed by a NOT gate.
  It acts the same way as the logical operation “and” followed by negation.
  The output is false only when all inputs are true.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 8: XOR Gate
XOR = exclusive-OR.
  Acts in the same way as the exclusive “either/or”.
  The output is true if either but not both of the inputs are true.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: XNOR Gate
XNOR = exclusive-NOR.
  Is a combination of the XOR followed by an inverter.
  Its output is true if both inputs are the same and false if the inputs are different.
Symbol:
Truth Table:
Input 1 | Input 2 | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 10: Lets Play!!! What logic gate marches the truth table?
Input 1 | Input 2 | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Input | Output
0 | 1
1 | 0
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Input 1 | Input 2 | Output
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 11: DIODE LOGIC: OR Gate
Makes use of the fact that diodes conduct current in one direction.
  This way, the diode acts as an electronic switch.
Consider the circuit below:
If both diode inputs are at logic 1, the output will still be logic 1.
This circuit thus effectively functions as an OR gate
  Assuming that logic 1 represents +5V while logic 0 represents the ground (0V)
  If both diode inputs A and B are left unconnected or held at logic 0, then the output Z will also be held at 0 by the resistor.
  However, if either input is raised to +5V, it’s diode would become forward biased and therefore conduct.
    This makes the output of the circuit logic 1

## Slide 12: DIODE LOGIC – AND Gate
Consider the circuit below:
  Case 2: either input is grounded (logic 0)
    Either or both of the diodes conduct and pull the output to logic 0
  This circuit thus effectively functions as an AND gate
  ASSUMPTIONS???
  Assuming that logic 1 represents +5V while logic 0 represents the ground (0V)
  Comparison to OR gate circuit:
    The diodes are reversed.
    The resistor pulls the output voltage to logic 1
  Case 1: both inputs left unconnected (logic 1)
    The output remains at logic 1

## Slide 13: Diode AND Gate Cont.
The resistor in the circuit is set to keep the output voltage at logic 1.
If any of the inputs is set at logic 0, the diode conducts and pulls the output voltage to logic 0.
If any of the inputs are set at logic 1, the associated diode is reverse biased and therefore doesn’t conduct.
For both inputs at logic 1, both diodes are reverse biased thus leaving the output at logic 1.
Input 1 | Input 2 | Output
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1