## Slide 1: CMP 2203
LECTURE 5

## Slide 2: Incompletely Specified Functions
Certain input conditions can never occur in some circuits
We “don’t care” whether their output is LOW or HIGH
Functions with don’t-care conditions are said to be incompletely specified
Choose them to be 0 or 1 in a way that gives the simplest implementation

## Slide 3: Multi-Level Synthesis

## Slide 4: Factoring
Use 3 AND gates and 1 OR gate

## Slide 5: Functional Decomposition
Decompose a two-level circuit into sub circuits
Sub circuits can be used in several places to create the entire circuit
E.g.
4 AND gates, 1 OR gate , 2 NOT gates.
Fan-in is 3 and 4 for AND gates and OR gate respectively
18 inputs ( wires) to all gates
Wiring takes large chip area. Need to reduce it.

## Slide 6: Functional Decomposition

## Slide 7: Functional Decomposition
2 additional gates (NOT and OR) but 15 inputs
Reduced biggest fan-in to 2
Cheaper circuit than previous 2 level one
Increased propagation delay  trade-off!
Decomposed realization of f !!

## Slide 8: Multi-Level NAND and NOR circuits
=
=
AND to NAND – invert output
OR to NAND – invert inputs (Lecture 3! Apply De Morgan’s)
Observe inversion on both ends of wire
Implement single inversions (NOT)
SOP = NAND-NAND
POS = NOR-NOR

## Slide 9: Analysing Multi-level Circuits
Get output at intermediate points and combine to SOP
Work this out. How many gates?

## Slide 10: Arithmetic Functions: Half- Adder
Addition of unsigned numbers
Half-adder adds two bits
Output is sum (LSB) and carry (MSB)
x | y | Carry | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
What gates represent the carry and sum?

## Slide 11: Full-Adder
How do we add more than two bits?
For each bit position, sum involves 3 bits: xi,yi and carry-in ci
Output is sum si and carry-out ci+1
ci | xi | yi | ci+1 | si
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 12: Decomposed Full Adder
Combines 2 half adders to form a full adder
Verify equivalence at home!

## Slide 13: Ripple Carry Adder
Multiple full adders in series
Each adder implements addition of one bit position
Each introduces a delay
Total delay is nΔt

## Slide 14: Adder/Subtractor
Recall 2’s complement: flip all bits ( 1’s complement) and add 1
1’s complement : can be done with NOT gates
Addition of 1 can be done by setting initial carry bit i.e. c0 to 1
More flexibility if we can apply a control input to select true value or complement of each bit using XOR gates
Recall: 2 input XOR gate
We can use e.g. x as a control:

## Slide 15: Adder/Subtractor
Choose control signal Add/subtract: If 0 = Add and if 1= subtract
Add/subtract also becomes initial carry bit
Connect each y output to XOR gate and control signal to select true or complement
N-bit full adder

## Slide 16: Homework!
Carry Look ahead adder
Multipliers
Dividers

## Slide 17: Multiplexers
N data inputs
Log2N select inputs
Output is one of data inputs depending on value of selector e.g. 4 to 1 multiplexer

## Slide 18: Synthesis of Functions using Multiplexers
Can be implemented with 4-to-1 multiplexer ; connect possible outputs to multiplexer input. Output selected based on value of w1 and w2
OR simplified to 2-to-1 by recognizing a pattern
Can be applied to synthesize any other logic circuit

## Slide 19: Example 2
Consider truth table for
Homework: when would you use multiplexers?

## Slide 20: Decoders
Decode encoded information
Has n inputs and 2n outputs
Selects only 1 output for each combination of inputs
Also has enable input used to disable the outputs. If En =0, no output is selected irrespective of value of select inputs. If En=1 one output is selected depending on input combination
Homework: when would you use a decoder?

## Slide 21: Demultiplexers
Opposite of multiplexer
Takes one input and places it onto multiple data outputs
Can be implemented with decoder
An n to 2n decoder can be used as a 1- to – n de-multiplexer
En is the data input and outputs are y0 to yn
Selection of w0w1 determines which of the outputs is set to En

## Slide 22: Continuous Assessment Test One
Material up to Lecture 6
Thursday 15th March, 10.00 AM
Closed Book
Zero tolerance to cheating
Missing the test = no grade. No exceptions
Good Luck!

## Slide 23: Handout
Read Chapter 5 and 6 of Brown